## Slide 1: Lecture 8 Micromouse PCB design guide

## Slide 2: Components Placement

## Slide 3
Place library for encoder/motor to (0,0) to make it symmetrical from left and right
Draw a middle reference line

## Slide 4
Use dimension layer to draw the outline of the mouse, make sure the length is not exceed 100mm to save cost

## Slide 5
Draw the guide line for the wall and posts in order to determine the sensor point angles later

## Slide 6
Place the components at proper position
Place sensors at proper position, make sure they point to proper location
Make sure the components won’t be blocked by motor mount/encoder

## Slide 7: Where should sensors point to?
Side sensors point to somewhere a little to the front of the post, when the mouse is at the center of the cell
Front sensors point outwards about 5-10 degrees, make so it won’t point to the side of the wall when at 1.5 cells away

## Slide 8: PCB drawing

## Slide 9: Settings
No mask for via>12 mills
Make 1 mill grid when drawing and parts placing

## Slide 10: Traces
MCU pins from LQFP package are 10-12 mill wide.
Try maximum tracer width for power/analog signal related trace
Thinner traces are OK for digital signal

## Slide 11: Trace thickness
Wider trace for high power intensive parts, ex. Vbat Power trace
Thinner for signal traces
Polygon may needed to give more area for power trace for thermo performance

## Slide 12: Trace style
good
bad
Shorter the possible
Less turn possible
45 degree turns

## Slide 13: Small via
12 mill via minimum
Good for signal trace
Better be masked

## Slide 14: Large Via
Larger via for power/thermo intensive trace/pad/polygon
Should not be masked
Drill shouldn’t bee too big

## Slide 15: Polygon
First to the First: Don’t make a single GND polygon for the entire PCB!!!!!
Why? Because it will transfer heat to temperature sensitive components easily from some heat intensive parts
You should place polygon selectively, only on those parts generate a lot of heat(5V LDO, motor driver) or the parts are sensitive with heat(MCU, analog device)

## Slide 16: Sample 1
Motor driver, GND polygon, on both sides

## Slide 17: Sample 2
Not make the polygon connected between 5V and MCU since MCU is temperature sensitive

## Slide 18: Distincted Ground
MGND
DGND
AGND
Don’t mix them before they reach the negative terminal of battery
AGND is temperature sensitive, make the trace avoid the hot area if possible

## Slide 19: MGND

## Slide 20: DGND

## Slide 21: AGND

## Slide 22: Questions?